## Slide 1
Bachelor thesis– Bern University of Applied Science
Freenet as a broker for „Medical“ IoT Data
25.06.2021
Student: Yannick Stebler
Professor: Prof. Dr. Emmanuel Benoist
Expert: Daniel Voisard

## Slide 2: Index
  Topic – Problem definition
  Goals
  Freenet (Broker)
  Architecture
  Attacks
  Prototype
  Problems
  Conclusion
  Questions

## Slide 3: Topic - Problem definition
  IoT devices are on the rise
  Many make everyday tasks easier
  Same problem for all of them
  Data Exchange via manufacturer
  Dependency to the manufacturer
  In case of bankruptcy device useless
=

## Slide 4: Goals
  Define new communication path
  Largely anonymous communication
  Protect the exchange of data
  Data access only for authorized parties
  Document the architecture of the new communcation path
  Implement it in a small prototype
    IoT sending device programmed with C
    Receiver programmed with C#

## Slide 5: Freenet (Broker)
  Free software
  Peer-to-peer platform for censorship-resistant communication
  Share files, browse and publish „freesites“ and chat on forums
  Encrypted communication
  Contribute to the network with bandwith and a portion of hard drive storage
  Is used as Broker in my Thesis
  More information on: https://freenetproject.org

## Slide 6: Architecture – Overview

## Slide 7: Architecture – Initialisation 1
  Freenet uses his own Protocol FCP – Freenet Client Protocol
  Input limitation of small IoT device
  Scratchable QR-code of upload URI (Path)

## Slide 8: Freenet – FCP Keys
  Freenet uses Keys to address files
    4 Types of Keys (CHK, SSK, USK, KSK)
    Only USK allows for update of Content (File)
  Usage of USK – Updateable Subspace Keys
    USK@public key hash,decryption key,crypto setting/user selected name/version
USK@VuHdPK~~8ArRcYhGU7JlibgTKSrnxLRH4jR1PCiHrUU,9SFpiAvN3pBYHyY~OSkwIk7wU33WYIU3a7Rt1fdmz~8,AQECAAE/temp/1

## Slide 9: Freenet – FCP Protocol
  ClientHello: On connection first message
  GenerateSSK: To generate new SSK/USK Keypair
  ClientPut: To upload Data to Freenet
  ClientGet: To request Data from Freenet
Send
ClientHello
Name=<Identifier>
ExpectedVersion=<Version>
EndMessage
Receive
ClientHello
Name=<Identifier>
ExpectedVersion=<Version>
EndMessage
Send
GenerateSSK
Identifier=<Identifier>
EndMessage
Receive
SSKKeypair
InsertURI=<SSKURIInsert>
RequestURI=<SSKURIRequest>
Identifier=<Identifier>
EndMessage
Send
ClientPut
URI=<USKURIInsert>
Metadata.ContentType=text/plain
PriorityClass=<Priority>
Identifier=<Identifier>
DataLength=<dataLenght>
Data
<DatatoUpload>
Receive
Send
ClientGet
URI=<USKURIRequest>
Identifier=<Identifier>
ReturnType=direct
PriorityClass=<Priority>
EndMessage
Receive
DataFound
Identifier=<identifier>
CompletionTime=<time>
StartupTime=<time>
DataLength=<dataLenght>
Global=false
Metadata.ContentType=text/plain
EndMessage
AllData
Identifier=ArduinoTemp2
CompletionTime=<time>
StartupTime=<time>
DataLength=<dataLenght>
Global=false
Metadata.ContentType=text/plain
Data
<DataRequested>

## Slide 10: Architecture – initialization 2
Steps:
  Scan QR-Code Sender on Receiver
  Register Receiver URI on Sender
  Both generate ECDH Keypair
  Exchange Public Keys
  Calculate Shared Secret and Generate new URIs
  Exchange Encrypted URIs
ClientPut
ClientGet
ClientPut
ClientPut
ClientGet
ClientGet
ClientPut
ClientPut
ClientGet
ClientGet
Shared Secret Secure Channel
GenerateSSK

## Slide 11: Architecture – Data transmission
Steps:
  Sender get stored information
  Read sensor data
  Encrypt sensor data and upload
  Receiver download data
  Decrypt sensor data
  Send receive confirmation to sender
ClientPut
ClientGet
ClientPut
ClientGet

## Slide 12: Attacks and Prevention
  Spoofing of the data
  Interruption of the data flow by flooding Freenet
  Phyiscal attack on IoT sender
  Physical attack on Freenet Node Hardware

## Slide 13: Prototype – Hardware
  Hardware used:
    Arduino Uno Wifi Rev.2
    LDR – Light Dependent Resistor
    DHT22 – Temp and Humidity sensor
    Breadboard
    Micro SD Card Reader Modul

## Slide 14: Prototype - Sender
  Written in Arduino IDE with C / C++
    Self written fcpClient Class
    Self written sdCard Class
    For each Sensor one Application
    Uses micro-ecc Library for ECDH

## Slide 15: Prototype – Receiver
  Written in Visual Studio with C#
    Currently Console Application
    Uses fcp2lib.NET Library as Freenet client
    Uses ECDiffieHellmanCng Class for ECDH Key generation
    Uses Aes Class for Encryption and Decryption

## Slide 16: Prototype - Status
  Connection to Freenet working
  Receiver registration working
  Exchange of Public Keys for ECDH working
  Generation of Shared Secret working
    But Shared Secret is not identical
    Not able to fix in time
  Limited programm space on Arduino – uses currently 87% of Sketch Space
  Great lack of documentation for the libraries (micro-ecc, fcp2lib.NET)
  Sadly no demonstration possible – not fully functional Prototype

## Slide 17: Conclusion
  Deffined / Developed a new communication path
  Anonymous and protected communication implemented
  Was a very demanding work
  Still a lot of room for improvement (Prototype)
  Was able to put many theoretical learnings into practice

## Slide 18: Questions